## Slide 1: Surfaces in neuroimaging

## Slide 2: Surfaces: what are they?
A surface is a special case of a graph (aka network)
  It has nodes and edges
  The structure of nodes and edges follow strict rules:
    A triangular mesh requires edges be part of 3-cliques
    A rectangular mesh requires edges be part of 4-cliques
  Video games and animated movies use meshes and 3d rendering
https://graphics.pixar.com/library/SigAsia2015/paper.pdf

## Slide 3: Surfaces can be designed by artists

## Slide 4: They can also be built by segmenting voxels

## Slide 6: How are they used for neuroscience?

## Slide 9: Fix issues with the surfaces

## Slide 10: Fundamentals: file format
”Index”, or vertex ID
Each Index has a coordinate in space
Triangles are 3-tuples of indices
Try it yourself! mris_convert rh.pial to rh.pial.asc
0.06 0.85 0.03
0.60 0.23 0.87
0.76 0.16 0.28
0.46 0.85 0.23
0.54 0.30 0.11
0.25 0.35 0.06
0.09 0.46 0.72
0.71 0.70 0.31
0.35 0.28 0.47
0.97 0.47 0.26
…
…
1 2 3
1 2 4
1 3 5
Coordinates in space
Index is implicit
Triangles!

## Slide 11: Mapping between volume and surface
Index
subvoxel spatial coordinate
Triangle
(Red) Voxel boundaries

## Slide 12: We can map lots of things to vertices
Curvature of the surface (scalar)
Thickness of the surface (scalar)
Optical flow (vector)
BOLD time series (time series)
Region labels (scalar)
Once mapped to a vertex, you can do whatever you want to the spatial coordinates

## Slide 14
LOL

## Slide 15: Registering to a template is great
But individuals still have different numbers of vertices!
AND they’re ordered differently!
Introducing: the standard surface

## Slide 17: Subsequent developments
Freesurfer binary formats are annoying to work with
GIfTI files were created as a “NIfTI for surfaces”
  Also turned out to be annoying: can only contain one surface
CIfTI files were invented to include 2 surfaces and some subcortical voxels
  They were an ad-hoc fork of the NIfTI-2 image format
  Only really supported by connectome_workbench
  Opaque and difficult development/standards